## Slide 1: Introduction to ArcGIS for Transport Applications

## Slide 2: Content
What is ArcGIS
Usefulness of ArcGIS
What can you do with ArcGIS
Navigating ArcGIS
ArcGIS Project
Create an ArcGIS project and load Data/Map
Data and map information
Attribute Table and its functionality
Selection, filtering, and subsetting data
Load spatial point data (Annual Average Daily Traffic data)
Using selection tool
Finding intersections
Add new fields to the intersection and intersection link attribute tables and populating them with relevant information

## Slide 3: ArcGIS development
ArcGIS is a Geographic Information System (GIS) software developed and maintained by Esri.
Esri – the Environmental Systems Research Institute
Esri aims to enable people to gain useful insights through geography
There are users in every country, with over a million active users across 350,000 organisations.
Currently available tools :
  ArcGIS Pro
  ArcGIS Online
  ArcGIS Enterprise

## Slide 4: ArcGIS Pro
64 Bit, multi-threaded
Simplified user interface
Integrated with ArcGIS Online
Combined 2D/3D experience
Multiple maps and layouts
All the analysis tools
Simple search and query

## Slide 5: What can you do with ArcGIS
ArcGIS is a mapping and spatial analysis platform
It helps users visualize, analyze, and manage geographic data
It is widely used in:
  Urban and transport planning
  Road safety analysis
  Infrastructure design
  Environmental impact assessment

## Slide 6: Use of GIS in Transport planning
Map road networks, traffic flows, crashes
Analyze accessibility and route efficiency
Identify risk areas (e.g., high crash zones)
Model travel behavior and infrastructure demand
Data types in ArcGIS
Vector data:
  Points (bus stops, crashes)
  Lines (road links, routes)
  Polygons (suburbs, zones)
Raster data:
  Used for terrain and land cover

## Slide 7: What can you do with ArcGIS?
Analysis
Analysis Ribbon
Geoprocessing pane
Model-builder
Python window
Network Analysis
Image and Raster Analysis
Visualization
Multiple layouts
Transparency
3D cartography
Map Series
Animation

## Slide 9: Navigating ArcGIS

## Slide 10: ArcGIS Project

## Slide 11: New ArcGIS Project Map > “Select a Location” > Enter the name “QLD_Roads_Tracks_Teaching”

## Slide 12: ArcGIS Project

## Slide 13: Project Folder

## Slide 14: QLD roads and tracks data

## Slide 15: QLD roads and tracks data
Data is available in the OneDrive folder

## Slide 16: Loading data Map > Add Data > Browse

## Slide 17: Loading Data “Select the folder” > “Select the layer”

## Slide 18: Loaded Qld roads and tracks data

## Slide 19: Attribute table for Qld roads and tracks data Right click on layer > Attribute Table

## Slide 20
Attribute table for Qld roads and tracks data

## Slide 21: Functionality of features in the attribute table Right click on a record in attribute table

## Slide 22: Selection/Filter/Subsetting features On the attribute table > Select “Select by Attributes

## Slide 23: Selection and Filtering criteria
Selection Criteria
Local government authority is only Brisbane city
  lga_left is equal “Brisbane City”
  lga_right is equal “Brisbane City”
Class of vehicles
  Symbol_class does not contain (“Bikeway”, “Walkway”, “Busway”, “Mall”, “Ferry”)

## Slide 24: Selected links from the layer Selected features are highlighted in blue in the attribute table and in the map

## Slide 25: Save selected features as a layer Right click on layer after selection > Selection > Make Layer from Selected Features

## Slide 26: Rename the new layer Right click on layer > Properties > General > Name > rename the layer

## Slide 27: Task 1 : Attribute filtering and separate layer
From the main.Queensland_roads_and_tracks map, filter the data based on the following attributes:
  “lga_name_left” and “lga_name_right” is “Gold Coast city”
  “class” contains “Motorway”, “Connector”, “Highway”, “Local” and “Secondary”
  “road_owner” is “TMR”
Save this selection as a separate layer named “Goldcoast_City”.

## Slide 28: Attribute Table options In the attribute table click on the three lines on the top right corner

## Slide 29: Attribute table for the selected layer In the attribute table click on the three lines on the top right corner > Select “Data Engineering”

## Slide 30: Loading Spatial Point Data (https://spatial-gis.information.qld.gov.au/arcgis/rest/services/Transportation/StateRoadInformation/MapServer/46) Paste the copied link into the path field

## Slide 31: Loading spatial point data from path Map > Add Data >From path

## Slide 32: Loading spatial point data from path Copy the html link for the data > paste the link under the Path

## Slide 33: Loaded spatial point data New layer named Average annual daily traffic 2020 in the contents pane

## Slide 34: Attribute table for spatial point data Right click on spatial point layer > Attribute Table

## Slide 35: Selecting features from polyline based on select tool Map > Select > Circle > Click and drag in map to select spatial data

## Slide 36: Save selected links as a separate layer From the selected features > right click on layer > selection > make layer from selected features

## Slide 37: Find intersections
The standard tools in ArcGIS do not support automatic identification of intersections and their corresponding intersecting links for spatial line data.
To successfully and easily complete this task it required to download a toolbox from the ArcGIS website.
Different programming languages can be used in ArcGIS to complete tasks without difficulty and to ensure that these tools are available for everyone the “ArcGIS code sharing” website is used. (https://codesharing.arcgis.com/)
Various spatial analysts have uploaded their solutions as toolboxes to be downloaded and uploaded into the ArcGIS project.

## Slide 38: Download and Add Toolbox
In the search bar type “intersection”
Under filters select “Tools”
Run the search
From the search results read each tool and its description
Find the best tool, for our task of identifying intersections and their links the tool “Line and Junction Connectivity”
Click the download button and store the zipped folder “IntersectionCount” in your ArcGIS project folder
Go to your project folder and unzip the downloaded folder

## Slide 39: Add the “IntersectionCount” toolbox to the ArcGIS project
Toolbar > Insert > Toolbox > Add Toolbox > in the window that opens go inside the “IntersectionCount” folder and select “Line And Junction Connectivity Tools.tbx”

## Slide 40: Loading “IntersectionCount” toolbox
Select Create Junction Connectivity Features
Line features : layer with line spatial data
Output Junction Feature Class and Output Junction And Line List Feature Class : layer names for the intersections (spatial point data) and links (spatial point data) of the output layers

## Slide 41
Spatial point data for the intersections.
In the attribute table “JUNC_ID” is the id assigned for the intersection automatically and “COUNT” is the number of links intersected in this intersection.
Spatial point data for the links associated with the intersections.
In the attribute table “JUNC_ID” is the id assigned for the intersection automatically, “FID_...” is the object id for the link associated with the intersection and “DIRECTION” contains a point for each line that connects to the junction and reports the direction of the line, either ‘From’ (start of the line) or ‘To’ (end of the line).

## Slide 42
Spatial point data for the intersections.
Spatial point data for the links associated with the intersections.

## Slide 43: Task 2: For the selected “Goldcoast City” layer find intersections and their respective links
For the “Goldcoast City” layer, zoom in, use the circle selection tool, and export the selected features as a separate layer.
Then, find the intersection points using the “IntersectionCount” toolbox.
Obtain the two output layers for the intersection and the links associated with the intersections.

## Slide 44: For a selected Intersection (node) identify the intersection type from reality (google maps) and store the information
Add a new field named Intersection_Type to the Brisbane_CBD_Intersect attribute table. Set the data type to Text, and save the changes by right-clicking on Fields: Brisbane_CBD_Intersect.
From the “Brisbane_CBD_Intersect” attribute table select an intersection by id (JUNC_ID is 1) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and right click on the intersection point in the map and select “Copy Coordinates”.
Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location. Open Street View using the icon in the bottom right corner of the google map.
From the street view point of view gather relevant information for the intersection, here it would be the Intersection type and record it in the “Brisbane_CBD_Intersect” layer attribute table under “Intersection_Type”.
If additional information needs to be recorded for the intersections, based on the information add a field to the “Brisbane_CBD_Intersect” layer and repeat steps from 2 to 5 until all intersections are populated.

## Slide 45: For a selected Intersection (node) identify the intersection type from reality (google maps) and store the information
Add a new field named Intersection_Type to the Brisbane_CBD_Intersect attribute table. Set the data type to Text, and save the changes by right-clicking on Fields: Brisbane_CBD_Intersect.
From the “Brisbane_CBD_Intersect” attribute table select an intersection by id (JUNC_ID is 1) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and right click on the intersection point in the map and select “Copy Coordinates”.
Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location. Open Street View using the icon in the bottom right corner of the google map.
From the street view point of view gather relevant information for the intersection, here it would be the Intersection type and record it in the “Brisbane_CBD_Intersect” layer attribute table under “Intersection_Type”.
If additional information needs to be recorded for the intersections, based on the information add a field to the “Brisbane_CBD_Intersect” layer and repeat steps from 2 to 5 until all intersections are populated.

## Slide 46: Add field “Intersection_Type” > For “Brisbane_CBD_Intersect” attribute table > Add > In “Fields: Brisbane_CBD_Intersect” > set “Field Name: Intersection_Type” > set “Data_Type : Text” from drop down list > Right click on “Fields: Brisbane_CBD_Intersect” and save

## Slide 47: For a selected Intersection (node) identify the intersection type from reality (google maps) and store the information
Add a new field named Intersection_Type to the Brisbane_CBD_Intersect attribute table. Set the data type to Text, and save the changes by right-clicking on Fields: Brisbane_CBD_Intersect.
From the “Brisbane_CBD_Intersect” attribute table select an intersection by id (JUNC_ID is 1) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and right click on the intersection point in the map and select “Copy Coordinates”.
Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location. Open Street View using the icon in the bottom right corner of the google map.
From the street view point of view gather relevant information for the intersection, here it would be the Intersection type and record it in the “Brisbane_CBD_Intersect” layer attribute table under “Intersection_Type”.
If additional information needs to be recorded for the intersections, based on the information add a field to the “Brisbane_CBD_Intersect” layer and repeat steps from 2 to 5 until all intersections are populated.

## Slide 48: In “Brisbane_CBD_Intersect” attribute table select feature JUNC_ID is 1 and right click on the record and select “Flash”.

## Slide 49: For a selected Intersection (node) identify the intersection type from reality (google maps) and store the information
Add a new field named Intersection_Type to the Brisbane_CBD_Intersect attribute table. Set the data type to Text, and save the changes by right-clicking on Fields: Brisbane_CBD_Intersect.
From the “Brisbane_CBD_Intersect” attribute table select an intersection by id (JUNC_ID is 1) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and right click on the intersection point in the map and select “Copy Coordinates”.
Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location. Open Street View using the icon in the bottom right corner of the google map.
From the street view point of view gather relevant information for the intersection, here it would be the Intersection type and record it in the “Brisbane_CBD_Intersect” layer attribute table under “Intersection_Type”.
If additional information needs to be recorded for the intersections, based on the information add a field to the “Brisbane_CBD_Intersect” layer and repeat steps from 2 to 5 until all intersections are populated.

## Slide 50: Go to the flashing intersection in the map and right click on the intersection point in the map and select “Copy Coordinates”.
The copied coordinates : 153.0263827°E 27.4771771°S

## Slide 51: For a selected Intersection (node) identify the intersection type from reality (google maps) and store the information
Add a new field named Intersection_Type to the Brisbane_CBD_Intersect attribute table. Set the data type to Text, and save the changes by right-clicking on Fields: Brisbane_CBD_Intersect.
From the “Brisbane_CBD_Intersect” attribute table select an intersection by id (JUNC_ID is 1) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and right click on the intersection point in the map and select “Copy Coordinates”.
Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location. Open Street View using the icon in the bottom right corner of the google map.
From the street view point of view gather relevant information for the intersection, here it would be the Intersection type and record it in the “Brisbane_CBD_Intersect” layer attribute table under “Intersection_Type”.
If additional information needs to be recorded for the intersections, based on the information add a field to the “Brisbane_CBD_Intersect” layer and repeat steps from 2 to 5 until all intersections are populated.

## Slide 52: Open a web browser, go to google.maps and paste the copied coordinates in the search bar and select the street view window in the bottom right corner of the google map

## Slide 53: Open a web browser, go to google.maps and paste the copied coordinates in the search bar and select the street view window in the bottom right corner of the google map

## Slide 54: For a selected Intersection (node) identify the intersection type from reality (google maps) and store the information
Add a new field named Intersection_Type to the Brisbane_CBD_Intersect attribute table. Set the data type to Text, and save the changes by right-clicking on Fields: Brisbane_CBD_Intersect.
From the “Brisbane_CBD_Intersect” attribute table select an intersection by id (JUNC_ID is 1) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and right click on the intersection point in the map and select “Copy Coordinates”.
Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location. Open Street View using the icon in the bottom right corner of the google map.
From the street view point of view gather relevant information for the intersection, here it would be the Intersection type and record it in the “Brisbane_CBD_Intersect” layer attribute table under “Intersection_Type”.
If additional information needs to be recorded for the intersections, based on the information add a field to the “Brisbane_CBD_Intersect” layer and repeat steps from 2 to 5 until all intersections are populated.

## Slide 55: From the street view gather relevant information for the intersection and record it in the attribute table of “Brisbane_CBD_Intersect” layer > Double click on cell adjacent to the relevant JUNC_ID is 1 under the field Intersection_Type and type “No Control” and save the ArcGIS project (Ctrl + S)

## Slide 56: For a selected Intersection (node) identify the links associated from reality (google maps) and store the information
Add the field “Link_Type” and “Capcity” in the “Brisbane_CBD_Intersect_Link” attribute table, assign data type to be “Text” and “Long”, respectively, save the changes by right clicking on the “Fields:Brisbane_CBD_Intersect_Link”.
From the “Brisbane_CBD_Intersect_Link” attribute table select an intersection by id (JUNC_ID is 1 and FID is 281460) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and click on the intersection links in the map.
Among the intersected links, click each one to identify the correct one by FID.
Right click on the intersection point in the map and select “Copy Coordinates”. Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location, select the street view window in the bottom right corner of the google map.
Based on the FID and the link in the map collect the information for “Link_Type” and “Capacity” and record it in the “Brisbane_CBD_Intersect_Link” layer attribute table under “Link_Type” and “Capacity”, respectively.
If additional information needs to be recorded for the links in the intersections, based on the information add a field to the “Brisbane_CBD_Intersect_Link” layer and repeat steps from 2 to 6 until all intersection links are populated.

## Slide 57: For a selected Intersection (node) identify the links associated from reality (google maps) and store the information
Add the field “Link_Type” and “Capcity” in the “Brisbane_CBD_Intersect_Link” attribute table, assign data type to be “Text” and “Long”, respectively, save the changes by right clicking on the “Fields:Brisbane_CBD_Intersect_Link”.
From the “Brisbane_CBD_Intersect_Link” attribute table select an intersection by id (JUNC_ID is 1 and FID is 281460) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and click on the intersection links in the map.
Among the intersected links, click each one to identify the correct one by FID.
Right click on the intersection point in the map and select “Copy Coordinates”. Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location, select the street view window in the bottom right corner of the google map.
Based on the FID and the link in the map collect the information for “Link_Type” and “Capacity” and record it in the “Brisbane_CBD_Intersect_Link” layer attribute table under “Link_Type” and “Capacity”, respectively.
If additional information needs to be recorded for the links in the intersections, based on the information add a field to the “Brisbane_CBD_Intersect_Link” layer and repeat steps from 2 to 6 until all intersection links are populated.

## Slide 58: Add field “Link_Type” and Capacity > For “Brisbane_CBD_Intersect_Link” attribute table > Add > In “Fields: Brisbane_CBD_Intersect” > set “Field Name: Intersection_Type” > set “Data_Type : Text” from drop down list > Right click on “Fields: Brisbane_CBD_Intersect” and save

## Slide 59: For a selected Intersection (node) identify the links associated from reality (google maps) and store the information
Add the field “Link_Type” and “Capcity” in the “Brisbane_CBD_Intersect_Link” attribute table, assign data type to be “Text” and “Long”, respectively, save the changes by right clicking on the “Fields:Brisbane_CBD_Intersect_Link”.
From the “Brisbane_CBD_Intersect_Link” attribute table select an intersection by id (JUNC_ID is 1 and FID is 281460) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and click on the intersection links in the map.
Among the intersected links, click each one to identify the correct one by FID.
Right click on the intersection point in the map and select “Copy Coordinates”. Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location, select the street view window in the bottom right corner of the google map.
Based on the FID and the link in the map collect the information for “Link_Type” and “Capacity” and record it in the “Brisbane_CBD_Intersect_Link” layer attribute table under “Link_Type” and “Capacity”, respectively.
If additional information needs to be recorded for the links in the intersections, based on the information add a field to the “Brisbane_CBD_Intersect_Link” layer and repeat steps from 2 to 6 until all intersection links are populated.

## Slide 60: In “Brisbane_CBD_Intersect_Link” attribute table select feature JUNC_ID is 1 (FID 281640) and right click on the record and select “Flash”.

## Slide 61: For a selected Intersection (node) identify the links associated from reality (google maps) and store the information
Add the field “Link_Type” and “Capcity” in the “Brisbane_CBD_Intersect_Link” attribute table, assign data type to be “Text” and “Long”, respectively, save the changes by right clicking on the “Fields:Brisbane_CBD_Intersect_Link”.
From the “Brisbane_CBD_Intersect_Link” attribute table select an intersection by id (JUNC_ID is 1 and FID is 281460) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and click on the intersection links in the map.
Among the intersected links, click each one to identify the correct one by FID.
Right click on the intersection point in the map and select “Copy Coordinates”. Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location, select the street view window in the bottom right corner of the google map.
Based on the FID and the link in the map collect the information for “Link_Type” and “Capacity” and record it in the “Brisbane_CBD_Intersect_Link” layer attribute table under “Link_Type” and “Capacity”, respectively.
If additional information needs to be recorded for the links in the intersections, based on the information add a field to the “Brisbane_CBD_Intersect_Link” layer and repeat steps from 2 to 6 until all intersection links are populated.

## Slide 62: Go to the flashing intersection in the map and click on the intersection links in the map.
The copied coordinates : 153.0263827°E 27.4771771°S

## Slide 63: For a selected Intersection (node) identify the links associated from reality (google maps) and store the information
Add the field “Link_Type” and “Capcity” in the “Brisbane_CBD_Intersect_Link” attribute table, assign data type to be “Text” and “Long”, respectively, save the changes by right clicking on the “Fields:Brisbane_CBD_Intersect_Link”.
From the “Brisbane_CBD_Intersect_Link” attribute table select an intersection by id (JUNC_ID is 1 and FID is 281460) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and click on the intersection links in the map.
Among the intersected links, click each one to identify the correct one by FID.
Right click on the intersection point in the map and select “Copy Coordinates”. Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location, select the street view window in the bottom right corner of the google map.
Based on the FID and the link in the map collect the information for “Link_Type” and “Capacity” and record it in the “Brisbane_CBD_Intersect_Link” layer attribute table under “Link_Type” and “Capacity”, respectively.
If additional information needs to be recorded for the links in the intersections, based on the information add a field to the “Brisbane_CBD_Intersect_Link” layer and repeat steps from 2 to 6 until all intersection links are populated.

## Slide 64: Of the intersected links click the link (Pop-up) and identify if it is the correct link, from FID and ObjectID, if not click the remaining links and find the correct link.

## Slide 65: For a selected Intersection (node) identify the links associated from reality (google maps) and store the information
Add the field “Link_Type” and “Capcity” in the “Brisbane_CBD_Intersect_Link” attribute table, assign data type to be “Text” and “Long”, respectively, save the changes by right clicking on the “Fields:Brisbane_CBD_Intersect_Link”.
From the “Brisbane_CBD_Intersect_Link” attribute table select an intersection by id (JUNC_ID is 1 and FID is 281460) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and click on the intersection links in the map.
Among the intersected links, click each one to identify the correct one by FID.
Right click on the intersection point in the map and select “Copy Coordinates”. Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location, select the street view window in the bottom right corner of the google map.
Based on the FID and the link in the map collect the information for “Link_Type” and “Capacity” and record it in the “Brisbane_CBD_Intersect_Link” layer attribute table under “Link_Type” and “Capacity”, respectively.
If additional information needs to be recorded for the links in the intersections, based on the information add a field to the “Brisbane_CBD_Intersect_Link” layer and repeat steps from 2 to 6 until all intersection links are populated.

## Slide 66: Open a web browser, go to google.maps and paste the copied coordinates in the search bar and select the street view window in the bottom right corner of the google map

## Slide 67: For a selected Intersection (node) identify the links associated from reality (google maps) and store the information
Add the field “Link_Type” and “Capcity” in the “Brisbane_CBD_Intersect_Link” attribute table, assign data type to be “Text” and “Long”, respectively, save the changes by right clicking on the “Fields:Brisbane_CBD_Intersect_Link”.
From the “Brisbane_CBD_Intersect_Link” attribute table select an intersection by id (JUNC_ID is 1 and FID is 281460) and right click on the record and select “Flash”.
Navigate to the flashing intersection on the map and click on the intersection links in the map.
Among the intersected links, click each one to identify the correct one by FID.
Right click on the intersection point in the map and select “Copy Coordinates”. Open a web browser, go to “https://www.google.com/maps” and paste the copied coordinates in the search bar and go to the location, select the street view window in the bottom right corner of the google map.
Based on the FID and the link in the map collect the information for “Link_Type” and “Capacity” and record it in the “Brisbane_CBD_Intersect_Link” layer attribute table under “Link_Type” and “Capacity”, respectively.
If additional information needs to be recorded for the links in the intersections, based on the information add a field to the “Brisbane_CBD_Intersect_Link” layer and repeat steps from 2 to 6 until all intersection links are populated.

## Slide 68: From the street view gather relevant information for the link associated with the intersection and record it in the attribute table of “Brisbane_CBD_Intersect_Link” layer > Double click on cell adjacent to the relevant JUNC_ID is 1 and FID is 281460 under the fields Link_Type and Capacity with “Freeway” and 2400, respectively. Save the ArcGIS project (Ctrl + S)

## Slide 69: Task 3: From the attribute tables for intersections and their respective links fill the relevant information
For the intersection and intersection link spatial information obtained for “Goldcoast city” add new fields.
For every intersection copy the coordinates and use it in google.maps and obtain information for the intersection and populate the intersection attribute table.
Similarly, for the intersection links use google.maps and obtain information for the intersection links and populate the intersection link attribute table.

## Slide 70: Data provided for the presentation and course
For this presentation ‘QSC_Extracted_Data’ contains Queensland roads and tracks data.
For this course ‘SEQ_Roads_Tracks_Teaching” is the ArcGIS project which contains spatial data for the links, intersections, links associated with intersections as separate layers named as “SEQ_roads_tracks”, “SEQ_Intersection” and “SEQ_Intersection_Links”, respectively.

## Slide 71: Thank You!